## Slide 1: Alternative Approaches and Routes Upper Charles Trail in Hopkinton
Peter LaGoy/Hopkinton Trails Club

## Slide 2: Summary and Conclusions: Alternative Approach
A Class 5 Stone Dust Shared Use Path (SUP) is:
  More consistent with the needs of Hopkinton for a Recreational Use-focused SUP
  Can be constructed at a lower cost
  Can be constructed more quickly
  i., e. Better, Cheaper, Faster
  and is consistent with Hopkinton’s history of community involvement

## Slide 3: Costs for Alternative Approaches Upper Charles Trail in Hopkinton
“Stone dust trails typically cost one tenth the cost of asphalt trails.”
Robert Weidknecht, Trail Expert formerly of Beals & Thomas
“The cost of the surface doesn’t have a major effect on trail costs”
VHB Engineers
The issue: We’ve been arguing which is correct, when both are correct.

## Slide 4: Actual Costs for the Completed Hopkinton Stone Dust Shared Use Paths (SUPs)
Trail Length Cost Cost per mile
Center Trail 0.6 mi $95,000 $158,000
Cntr Tr Ph 2 0.2 mi $40,000 $200,000
Echo Tr 0.6 mi $65,000 $108,000
Hughes Tr 0.45 mi $80,000 $178,000
Mdl Sch XC 0.4 $63,000* $158,000
Total 2.25 mi $343,000 $152,000
*Cost to complete; not final at this time

## Slide 5: Costs for Engineered Stone Dust SUP
Hopkinton 2.25 mi $152,000/mi
Holliston 6.4 mi $50,000/mi
Medfield 1.3 mi $181,000/mi
Summary of Costs for Stone Dust SUP: <$200,000 per mile as estimate

## Slide 6: Costs for DOT Preferred/Asphalt Paved Shared Use Path (SUP)
B&T and VHB engineering estimate: $2,000,000 per mile as estimate
Typical Road cost estimate: $5,000,000 per mile as estimate
DOT Preferred SUP is < half road width, without shoulder, curbing, and extensive drainage
Summary of Costs for DOT Preferred/Asphalt Paved: $2,000,000 per mile as estimate

## Slide 7: Basis for Difference in Cost
Stone Dust SUP
  Follows state guidance but only needs to meet town requirements
  Limited survey/wetlands mapping/plans
  Typically design/build approach
DOT-preferred Asphalt or Stone Dust SUP
  Bureaucratic Public Works Project (mini-road)
  Detailed survey/wetlands mapping/10%, 25% 75% 100% plans
  Typically Bid Process
  Extensive Stormwater Management/Fencing/Signage
SUPs just different; neither is better for all uses

## Slide 8: VHB Matrix

## Slide 9: VHB Matrix - Components
Air Quality Impacts
Noise Impacts
Flood Plain
Certified Vernal Pools (In Hopkinton, should be any Vernal Pool)
Threatened & Endangered Species
ACEC
National Registry
Hazardous Waste Site

## Slide 10: DOT-preferred Surveyed path vs Center-flagged path: Same trail but large cost difference.

## Slide 11: Summary: Stone dust Class 5 SUP costs one tenth of a DOT-preferred asphalt Class 5 SUP
Class 5 Stone Dust Shared Use Path
  Meet Town’s Requirements; Generally follows MassDOT Guidance
  Cost: $200,000 per mile
Class 5 Asphalt-Paved Shared Use Path
  Bureaucratic Public Work Project Adhering to MassDOT Guidance
  Cost: $2,000,000 per mile; $380,000 direct cost to Hopkinton
Maintenance costs of stone dust typically lower
Designed and Built Differently; Neither Better for All Uses

## Slide 12: Primary Trail Purposes
Stone Dust SUP
  Recreation, including
    Pedestrian Use (Dog walking)
    Running
    Leisure bike riding
    Wheelchair use
    Equestrian Use
DOT-preferred Asphalt SUP
  Commuting, including
    Bike commuting
    Fast wheelchairs
    In-line skates

## Slide 13: Summary: Stone Dust and DOT-preferred Trails (typically asphalt) are both Shared Use Paths but with different focuses.
Stone Dust SUP – Recreational Focus
  Meets town needs
  Examples are Hopkinton Trails, Holliston Trail, and Milford Trail
DOT-preferred Asphalt SUP – Bike Commuter Focus
  Overkill for Hopkinton
  Examples are Minuteman Trail, Bruce Freeman Trail, and other Urban Trails

## Slide 14: Summary and Conclusion: For Hopkinton, a Recreation-Focused Stone Dust Class 5 SUP is Better; Cheaper; Faster
Recreational Use-Focused SUP versus Commuter-Focused SUP
  Hopkinton/Holliston/Milford vs. Minuteman/Freeman/Urban trails
Cost: $200,000 per mile versus $2,000,000 per mile ($380,000 per mile directly to town, assuming TIP grant received)
Timing: Stone Dust SUP construction in 2022; DOT-preferred asphalt SUP in 2027???
Hopkinton Factor
  Hopkinton history of volunteerism – Existing Trails/Gazebo/West Main Plantings/Fountain on Common

## Slide 15: Trails Club Alternative Route
North section
  West of Charlesview Neighborhood
  Uses town-owned land plus 3 (or 2) private parcels (owners of 2 parcels not previously contact but willing to work with town)
  Wooded versus along roadway
Middle section (Hughes to Echo) consistent with UCTC concept
South section
  Uses Existing Echo Trail (0.6 mi of Class 5 stone dust SUP)
  Proposes use of pedestrian bridge over roadway

## Slide 16: North Section

## Slide 17: Daniel Road Alternatives
Main alternative (“A”) crosses Gorman land
  Route stays in woods
  Chapter 61 land
Alternative B uses town roadway easements and land and crosses Daniel Road
  Not ideal but possible as temporary solution
  Avoids Gorman land
  Daniel Road is a cul de sac so traffic limited

## Slide 18: Daniel Rd Alternatives

## Slide 19: South Section

## Slide 20: Benefits of Alternative Route
No crossings of major roadways
  Enhanced safety
  Much less impact on traffic
Less impact on residents
  5 Landowners directly affected by Alternative
  15+ Homeowners and front lawns directly affected by UCTC Concept
More consistent with town desire for wooded path
Uses existing Class 5 stone dust SUPs

## Slide 21: Conclusion: Trails Club Alternative
Alternative Approach: Stone Dust, Recreational Use-Based SUP
  Stone dust better for many recreational uses
  Much cheaper to build and maintain
  Trail work can start much sooner
Alternative Route: Around Charlesview and south on Echo to Milford
  Much safer, with no major roadway crossings
  Lower impact on residents
  Wooded route